## Slide 1: Experimenting with Embedded Swift on ESP32-C6 and I2C sensor
By: Yeo Kheng Meng (@yeokm1)
https://github.com/yeokm1/swift-embed-experiment
iOS Dev Scout (23 July 2025)

## Slide 2: Who am I?
Yeo Kheng Meng
Embedded Security Researcher
  Centre for Strategic Infocomm Technologies (CSIT)
  MINDEF Technical Agency
10 years Embedded experience in private and public sectors
  PCB Hardware Design
  Microcontroller Firmware
  Embedded Linux

## Slide 3: What is Embedded Swift?
First announced in WWDC 2024: https://www.youtube.com/watch?v=LqxbsADqDI4
Swift for resource-constrained microcontrollers like ESP32, RPi Pico, STM32

## Slide 4: Before and after Embedded Swift
Before
  Swift binary needs an operating system: iOS, MacOS, Linux, Windows
  Runs on relatively performant hardware
    GHz-class multi-core CPUs
    GBs of RAM
    GBs to TBs storage
After
  Bare-metal microcontrollers (MCU) with no OS or relatively-small real-time OS
  Resource-constraint hardware
    Mhz-class single/dual-core CPU
    Kilobytes to low Megabytes RAM
    Kilobytes to low Megabytes storage

## Slide 5: Embedded Swift vs conventional Swift
Experimental support
Subset of conventional Swift
  >>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>
  No Foundation
  No print and String floating-point support
  Xcode IDE does not support Embedded Swift
BridgingHeader.h
  To import C SDK or libraries
  No support for Objective-C
https://docs.swift.org/embedded/documentation/embedded/languagesubset/
https://github.com/swiftlang/swift/blob/main/docs/EmbeddedSwift/EmbeddedSwiftStatus.md

## Slide 6: Presentation Topics
Hardware
Running Apple’s Embedded Swift example
Communicating with an environmental sensor
Using LLMs to aid in this project
Challenges encountered
Personal conclusion on Embedded Swift

## Slide 7: Board selection
Only a few MCU types are supported
Consult Swift Embedded examples Github
  https://github.com/swiftlang/swift-embedded-examples/
Supported MCUs
  Espressif ESP32-C6
  Raspberry Pi Pico 1/2 (W)
  Nordic nRF52840
  STM32F746G
Why ESP32-C6-DevKitC-1?
  Relatively low-cost SG$15
  Pi Pico is cheaper at SG$6 but troublesome for development
    Need to press BOOTSEL button on every flash
    Requires separate SG$20 debug probe for ease of development

## Slide 8: ESP32-C6-DevKitC-1 development board
Created by Espressif systems
Using ESP32-C6-WROOM-1 module
Onboard WS2812 RGB LED
USB-C Ports
  Native USB Debug/Serial port
  UART-USB through Silicon Labs CP2102

## Slide 9: Hardware breakdown
ESP32-C6-DevKitC-1 (breakout board)
ESP32-C6-WROOM-1 Module
ESP32-C6 Quad Flat No-leads (QFN-40)
ESP32-C6-WROOM-1 module used to speed up hardware development
  Flash options: 4/8/16MB
ESP32-C6 microcontroller specs
  Dual-core RISC-V, LP: 20Mhz, HP:160Mhz
  SRAM, LP: 16KB, HP: 512 KB
  2.4Ghz Wi-Fi 6, Bluetooth 5
  SPI, I2C, UART, GPIO

## Slide 10: Using Apple’s lightstrip example
Light strip made of multiple WS2812 RGB LED
WS2812 uses single-wire daisy-chain protocol
Cycles through different colours
Install Swift development snapshot
  brew install swiftly
  swiftly install --use main-snapshot
  swiftly list
Install ESP-IDF:
  git clone -b v5.4.2 --recursive https://github.com/espressif/esp-idf.git
  cd ~/esp/esp-idf
  ./install.sh esp32c6

## Slide 11: Modify example to use onboard RGB LED
Modify example
  cd esp32-led-strip-sdk
  Change to IO8
Build project by invoking MCU’s SDK
  . $HOME/esp/esp-idf/export.sh
  idf.py set-target esp32c6
  idf.py build
  idf.py flash
  idf.py monitor

## Slide 12: Bosch BME680 Sensor
Temperature, Pressure, Humidity, Gas sensor
3.0 x 3.0 x 1 mm
Connection: I2C, SPI
I2C - Inter-Integrated Circuit bus
  Intra-board communication
  2-wire protocol
    Serial data line (SDA)
    Serial clock line (SCL)
  One master – multiple slave
  Typical speed: 100kbps (standard), 400kbps (fast)

## Slide 13: Asking LLMs – ChatGPT + Claude + Copilot
LLMs could not generate satisfactory Swift code for this purpose
Observations of LLM-generated Embedded Swift code
  Swift code meant for iOS or MacOS
  Provide empty functions for you to fill
  Hallucination of none-existent embedded functions
Possible Reasons
  Embedded Swift only released last year and still experimental
  Majority of online Swift code is meant for iOS/MacOS
  No official Apple examples of Embedded Swift ESP32 I2C communication
  Embedded code is a niche field with less code online, mostly C/C++

## Slide 14: Strategy
Write all Wrapper code in C
  Avoid unsafe code and C data structures in Swift
Get Embedded Swift to call the C-wrapper code
Ask LLM to translate C wrapper code to Swift
Suggested by ChatGPT

## Slide 15: I2C Communication from BME680 datasheet
Master always initiates the communication
Data transfers usually works on registers
BME680 I2C Write register packet frame
  Master writes slave address
  Master writes register address (control)
  Master writes data
  Master sends STOP signal
BME680 I2C read register packet frame
  Master writes slave address
  Master writes register address (control)
  Master sends STOP signal
  Slave writes slave address
  Slaves write data
  Slaves sends STOP signal

## Slide 16: Embedded I2C firmware flow
Usually provided by manufacturers
  Bosch BME680 I2C driver library
    You have to implement I2C read/write and delay functions and pass to the library
  Espressif Board Support Package (ESP-BSP)
    API to use MCU hardware features
You have to develop
  Bridge between the I2C driver and BSP
  Call the necessary library/BSP functions
BME680 I2C library
int8_t bme68x_init(struct bme68x_dev *dev);
int8_t bme68x_get_data(uint8_t op_mode, struct bme68x_data *data, uint8_t *n_data, struct bme68x_dev *dev);
Function Pointers to provide in init:
int8_t (*bme68x_read_fptr_t)(uint8_t reg_addr, uint8_t *reg_data, uint32_t length, void *intf_ptr);
int8_t (*bme68x_write_fptr_t)(uint8_t reg_addr, const uint8_t *reg_data, uint32_t length, void *intf_ptr);
void (*bme68x_delay_us_fptr_t)(uint32_t period, void *intf_ptr);
ESP-BSP
int i2c_master_transmit_receive(i2c_master_dev_handle_t i2c_dev, const uint8_t *write_buffer, size_t write_size, uint8_t *read_buffer, size_t read_size, int xfer_timeout_ms)
int i2c_master_multi_buffer_transmit(i2c_master_dev_handle_t i2c_dev, i2c_master_transmit_multi_buffer_info_t *buffer_info_array, size_t array_size, int xfer_timeout_ms);
void ets_delay_us(uint32_t us);
C-wrapper
Call BME680 init, pass your implement I2C read/write and delay function pointers
Call library get_sensor_data()
Library will use your implemented I2C read/write and delay functions

## Slide 17: Embedded Swift compilation process
Swift code
C code
Swift .o object code
C .o object code
Swiftc
RISC-V GNU toolchain
Binary
ESP-IDF + ESP-BSP + linker

## Slide 18: Demo of C-wrapper
cd esp32-bme680-c-wrapper
. $HOME/esp/esp-idf/export.sh
idf.py set-target esp32c6
idf.py flash && idf.py monitor

## Slide 19: Implement C pointer functions using ESP-BSP
I2C read:
  Passthrough to BSP i2c_master_transmit_receive()
I2C write:
  Create array of i2c_master_transmit_multi_buffer_info_t
  Send using BSP i2c_master_multi_buffer_transmit
Delay
  Passthrough to BSP ets_delay_us(period);

## Slide 20: Swift calls C-wrapper
bme680_wrapper.c
Main.swift

## Slide 21: Relevant C-Swift conversion
Calling C functions from Swift
  Mapping C parameters to Swift Unsafe types
    UnsafePointer<Type>, UnsafeMutablePointer<Type>
    UnsafeRawPointer, UnsafeMutableRawPointer
  https://developer.apple.com/documentation/swift/using-imported-c-functions-in-swift
Import C macros
  “C macros that are more complex than simple constant definitions have no counterpart in Swift. ”
  https://developer.apple.com/documentation/swift/using-imported-c-macros-in-swift

## Slide 22: Translate pointer functions in C-wrapper to Swift-wrapper
bme68x_wrapper.c
bme68x_wrapper.swift

## Slide 23: Avoiding direct use of UnsafeMutablePointer
UnsafeMutablePointer allocated on heap
Repeated allocation and deallocation on heap bad for MCUs
  Slower
  May cause memory fragmentation
  Potential failure to allocate as memory resources limited on MCUs
Asked AI for a heap-less alternative
  Use withUnsafeMutablePointer and mutating to temporarily access variables as UnsafeMutablePointer for duration of closure without heap allocation
  https://developer.apple.com/documentation/swift/withunsafemutablepointer(to:_:)

## Slide 24: Heap-less option
Manually allocating UnsafeMutablePointer on heap
Scope withUnsafeMutablePointer

## Slide 25: Demo of Swift-wrapper
cd esp32-bme680-swift-wrapper
. $HOME/esp/esp-idf/export.sh
idf.py set-target esp32c6
idf.py flash && idf.py monitor

## Slide 26: Troubleshooting with Logic Analyzer
Tapping I2C lines with Saleae Logic Pro 8
Reading and analyze signals with Logic 2

## Slide 27: Conclusion
Embedded Swift still experimental after 1 year -> Not ready for production
Mismatch between goals of Swift (higher level languages) vs embedded platforms
  High-level languages generally discourage using low-level features like UnsafePointers
  Embedded engineers frequently use low-level access for performance/memory optimisation
Embedded devices are not as vertically integrated as Apple macOS/iOS devices
  Heavy dependence on vendor stacks and C libraries
  Not many MCUs are supported other than ESP32, RPi Pico, STM32
Most Embedded stuff are aimed at C/C++
  SDK and Debugging tools
  Documentation
-> Swift adoption by MCU embedded engineers would be very challenging